## Slide 2
Chapter 13
Vehicle Maintenance Inspection

## Slide 3: Introduction
Regular inspection and maintenance
  Allows for safe and reliable operation
Common types of inspection
  Basic inspection
  In-depth inspection
  State safety inspection
  Certified used car inspection
  Vehicle prepurchase inspection

## Slide 4: Introduction
Document inspection process
  Paper forms
  Electronic forms
Technicians need to:
  Take detailed notes/pictures
  Follow manufacturers’ procedures and specifications
Courtesy of John Griffin, CEO of Drive Cherry.

## Slide 5: Introduction
Cherry Inspect
  www.drivecherry.com
  Electronic inspection system
  Can be 40% more efficient than paper inspection forms
  Can include notes and pictures
    Evidence for decisions made
Courtesy of John Griffin, CEO of Drive Cherry.
Courtesy of John Griffin, CEO of Drive Cherry.

## Slide 6: LO 13-1: Perform in-vehicle inspection.
In-vehicle concerns
  Many drivers overlook
  Others ignore
Driving vehicle into service bay, check:
  Instrument cluster
  Warning lights
  How pedals feel
  Engine sounds
  Illuminated malfunction indicator lamp (MIL) = need to check for any diagnostic trouble codes (DTCs) with scan tool

## Slide 7: LO 13-1: Perform in-vehicle inspection.
Brake pedal
  Any changes to the resistance can indicate a problem
  If the pedal is low or hard, do not drive the vehicle.
Unusual brake sounds
  High-pitched scrape noise
  Grinding noise
  Could indicate brake problems

## Slide 8: LO 13-1: Perform in-vehicle inspection.
Service/parking brake
  Holds vehicle in position when parked
  Should be checked during routine inspections
Checking parking brake
  Apply brake and observe how far vehicle travels
  Going all the way/near its stop = brake needs further attention
  Do not test parking brake in below-freezing temperatures

## Slide 9: LO 13-1: Perform in-vehicle inspection.
Instrument panel warning lamps
  Indicate faults with various systems
  Warning lamp per system
  A MIL will be illuminated when a fault is detected.
Starting the vehicle
  Observe the lights
  MILs often turn on briefly while checking for faults, then turn off
  On-board diagnostics generation II (OBD-II) does the same
    No DTCs stored = light will go off within a few seconds

## Slide 10: LO 13-1: Perform in-vehicle inspection.
OBD-II system
  Tests and analyzes engine’s systems
    While vehicle is being operated
  Will set and store DTC if a fault is detected
During in-vehicle inspection
  Retrieve DTCs if any MILs are illuminated
  The code will help you diagnose any faults

## Slide 11: LO 13-1: Perform in-vehicle inspection.
Horn
  Operated by a relay or by vehicle body control module (BCM)
  Located in front of vehicle
    Behind grill or bumper
  Some cars have two horns
    One has a lower pitch than the other
Check horn quickly before driving vehicle into the shop

## Slide 12: LO 13-1: Perform in-vehicle inspection.
Interior lights
  Courtesy lights
    Turn on with use of key or after opening driver’s door
  Dome lights
    Turn on with use of key or after opening driver’s door
    Can be switched on when door is closed
  Vanity lights
    Usually on back of visor; switched on
  Map lights
    Usually turn on when moved into a position in which they can be used

## Slide 13: LO 13-2: Perform fluid inspection.
Underhood inspection
  Perform at manufacturer’s recommended intervals or prior to a long driving trip
  Check for low fluid level, torn belt
  Can prevent many future problems

## Slide 14: LO 13-2: Perform fluid inspection.
Vehicle fluids
  All must be at right level
  Use manufacturer’s recommended type
  Nearly all fluids get old and wear out
    Except some automatic transmission/transaxle fluids
    Replacement is necessary
  Different fluids show age differently.

## Slide 15: LO 13-2: Perform fluid inspection.
Engine oil levels
  Too low: oil pump starves for oil
  Too high: crankshaft churns oil to foam
Both cause lack of lubrication
  Leads to damage throughout engine

## Slide 16: LO 13-2: Perform fluid inspection.
Checking engine oil levels
  Vehicle must be on level surface
  Engine OFF
Use a dipstick
  Full/add or min/max levels marked
  Difference between full and add marks
    Differs by vehicle
    Usually 1 quart (0.9 liter)
    Can reach 2 quarts (1.9 liters)

## Slide 17: LO 13-2: Perform fluid inspection.
Dipstick
  Read horizontally
  Check both sides
  Lower level usually more accurate

## Slide 18: LO 13-2: Perform fluid inspection.
Oil-life monitoring (OLM) system
  Check to determine if time for oil change
  Indicates remaining % of oil life
Vehicles without OLMs
  Consult service information
  Recommended mileage/time interval between changes

## Slide 19: LO 13-2: Perform fluid inspection.
If engine oil needs to be changed
  Still check oil level with dipstick
  Low reading could = leak or engine is using oil
  Both situations require further investigation
Refer to Chapters 18 and 19 for more information on engine lubrication.

## Slide 20: LO 13-2: Perform fluid inspection.
Coolant
  Transfers excessive heat
    From engine  radiator
  Check whenever checking engine oil
Checking coolant levels
  Some vehicles have tank with hot/cold markings
  Allows for check without having to remove the cap

## Slide 21: LO 13-2: Perform fluid inspection.
Coolant level check, cont’d
  Other vehicles have a transparent overflow tank
    Can view fluid hot/cold levels
  Older vehicles
    May require removing radiator cap
    Confirm coolant level is about 1.5 inches (38.1 millimeters) below filler neck

## Slide 22: LO 13-2: Perform fluid inspection.
Checking coolant freeze point
  Insufficient antifreeze can  coolant freezing  cooling system components expanding and cracking
  Measured with antifreeze hydrometer or refractometer

## Slide 23: LO 13-2: Perform fluid inspection.
Brake fluid
  Check level when oil level is checked
  Hygroscopic and hydraulic braking systems depend on it
  Hygroscopic brake fluids absorb water from atmosphere
    Change every 2 to 4 years
  Brake fluid tester or brake fluid test strips
  Check brake master cylinder reservoir or separate fluid reservoir

## Slide 24: LO 13-2: Perform fluid inspection.
Power steering fluid
  Engine should be idling
  Fluid should be hot
  Fluid reservoir or separate container
Check
  Appearance
    Dark fluid = needs to be changed
  Level with dipstick
    Connected to filler cap

## Slide 25: LO 13-2: Perform fluid inspection.
Automatic transmission/transaxle fluid
  Too low = slipping and shift timing faults
  Too high = fluid churns and aerates
Checking levels
  Engine running
  Transmission fully warmed
  Vehicle in Park or Neutral
  Use dipstick located under the hood, near front of the transmission

## Slide 26: LO 13-2: Perform fluid inspection.
Always use the specified type of transmission fluid
Use a funnel to add the fluid
  Through dipstick tube
  Add only small amounts at a time

## Slide 27: LO 13-2: Perform fluid inspection.
Vehicles without dipsticks
  Follow service information
  Some have a fill plug (or “level plug”)
    On side of transmission

## Slide 28: LO 13-2: Perform fluid inspection.
Diesel exhaust fluid (DEF)
  Used by some diesel-powered vehicles
  Helps reduce nitrogen oxides in exhaust
  Consumed over time  replenished periodically
  Filler cap
    Often located under the hood
    Usually blue

## Slide 29: LO 13-2: Perform fluid inspection.
Windshield washer fluid
  Important for the safety of the driver.
  Reservoir is usually under the hood
  May have separate rear reservoir for rear window
    Usually somewhere in rear hatch or trunk
  Check level at each vehicle service

## Slide 30: LO 13-3: Perform belt, hose, and air filter/cabin air filter inspection.
Engine drive belts
  Operate engine accessories
    Example: water pump, alternator
  Broken belts/belts that come off = engine quickly overheats

## Slide 31: LO 13-3: Perform belt, hose, and air filter/cabin air filter inspection.
Two belt types
V-belts
  Inside V-shaped groove in pulley
  Wedge into its sides
Serpentine-type belts
  Have grooves that are exact reverse of grooves in pulley’s outer diameter
  Usually recommend also replacing tensioner

## Slide 32: LO 13-3: Perform belt, hose, and air filter/cabin air filter inspection.
Visually inspect driver belts whenever you are under the hood
Check for:
  Cracks
  Oil soaking
  Glazing
  Tears
  Bottoming out

## Slide 33: LO 13-3: Perform belt, hose, and air filter/cabin air filter inspection.

## Slide 34: LO 13-3: Perform belt, hose, and air filter/cabin air filter inspection.
Hoses
  Usually two large radiator hoses
    Upper and lower
  Some smaller heater hoses
Inspection
  Engine should be cool
  Feel hoses for consistent firmness
    Not too soft or hard
  If hot, look for bulging in hoses

## Slide 35: LO 13-3: Perform belt, hose, and air filter/cabin air filter inspection.
Air filter
  Protects engine from dust, grit, etc.
  Location varies by fuel system type
    Check service information
Inspection
  Check air cleaner housing and ductwork
  Look for cracks or holes
  Remove filter, hold up to light
    No light = clogged, needs replacement

## Slide 36: LO 13-3: Perform belt, hose, and air filter/cabin air filter inspection.
Cabin air filter
  Part of HVAC system, in air box
  Access point differs by vehicle
Inspection
  During every service
  Replacement interval according to manufacturer
  Hold up to light as with air filter
  Also check for cracks, tears, etc.

## Slide 37: LO 13-4: Perform under-vehicle inspection.
Under-vehicle inspection
  Visual inspection of major systems
  Vehicle on hoist
  Observable problems
    Tire issues, leaks, worn parts, structural damage
  Document inspection results

## Slide 38: LO 13-4: Perform under-vehicle inspection.
Tire inspection
  Checked for pressure, wear patterns, cuts, and tread depth
Tire air pressure
  Check every 3 months or every oil change
  Under- and over-inflated tires wear out sooner
  Normal pressure varies by vehicle
    Check tire placard

## Slide 39: LO 13-4: Perform under-vehicle inspection.
Maximum tire pressure
  For that tire
    Not the vehicle
  Never go over the maximum
Inflated with compressed air or nitrogen

## Slide 40: LO 13-4: Perform under-vehicle inspection.
Tread depth and wear
  Inspect for wear
  Measure depth at least three places per tire
  Identifies uneven wear in tread
Inspect tire
  Look for damage, bulges
  Plug patches only work if hole diameter is < 0.25 in. (6 mm)
  Feel tire for bulges, be wary of steel cords

## Slide 41: LO 13-4: Perform under-vehicle inspection.
Tire age
  Usually 6- to 10-year life
  Locate DOT tire date code
    Tire’s sidewall
  First two digits = week of manufacture
  Last two digits = year
  E.g., 3020 = 30th week of 2020
Refer to Chapter 41 for more on tires

## Slide 42: LO 13-4: Perform under-vehicle inspection.
Manual transmission/transaxle/ transfer case fluid
  Preventative check
  Fill plug usually on side of transmission/ transaxle
  Remove plug, if fluid comes out, reinsert
  If no fluid, use finger to feel for level
  Above 0.25 in. (6 mm) from bottom is OK
    Lower = add until fluid is even with bottom of fill hole

## Slide 43: LO 13-4: Perform under-vehicle inspection.
Differential/transfer case fluid level
  Similar to checking transmission fluid
  Refer to service information for differences/vehicle specifics
Differentials and transfer cases
  Often no drain plug
  Specific bolts/covers may need to be removed

## Slide 44: LO 13-4: Perform under-vehicle inspection.
Checking for fluid leaks
  Clean shop floor before driving vehicle in, makes leaks clear
Become familiar with each fluid’s color, feel, and smell
Brake fluid
  Clear or light amber (DOT 3/DOT 4), purple (DOT 5)
  Slippery, has slight acidic smell
Automatic transmission fluid
  Reddish (normally) or clear/amber (some manufacturers)
  Slippery, oily, has oily smell

## Slide 45: LO 13-4: Perform under-vehicle inspection.
Power steering fluid
  Red if uses automatic transmission fluid
  Clear if uses power steering fluid
Coolant
  Normally green, orange, yellow (GM uses red/light red)
  Slippery, has sweet/syrupy smell
Engine oil
  Clear, brown, or black
  Very slippery, thick, has oily smell

## Slide 46: LO 13-4: Perform under-vehicle inspection.
Gear oil
  Light brown
  Very slippery, has oily smell
Gasoline
  Clear
  Evaporates easily, has distinct odor
Diesel
  Dirty clear
  Thin, has oily smell

## Slide 47: LO 13-4: Perform under-vehicle inspection.
Checking for leaks
  Ask customer about any smells
  Ideally with vehicle on lift, engine off
  Use flashlight to look for drips/wetness
  Always look to top of wet are for leak source
  Some leaks can send fluids far away from source
  If none found, start engine and wait a few minutes
    Inspect, keeping away from hot and moving parts
    Shut down engine and check again

## Slide 48: LO 13-4: Perform under-vehicle inspection.
Steering system inspection
  Best if vehicle is on lift
  Look for wear and damage
  Wiggle each wheel while someone else feels for any play in steering joints

## Slide 49: LO 13-4: Perform under-vehicle inspection.
Check suspension system for:
  Worn or torn parts
  Tears or displacement in dust boots
  Leaks in shock absorbers
  Cracks/bulging in brake hoses
  Kinks/rust in brake lines
  Excessive play in wheel bearings

## Slide 50: LO 13-4: Perform under-vehicle inspection.
Check drive axles and driveshafts for:
  Worn out joints
  Bent/damaged axles
  Cracked, torn, or leaking dust boots/CV joints
  Excessive movement, dents, or bends, in the driveshaft
  Leaks around the differential
  Check rear shock absorbers, leaf springs, brake hoses, and lines

## Slide 51: LO 13-4: Perform under-vehicle inspection.
Engine inspection
  Torn or cracked motor mounts, coolant hoses, belts
Transmission inspection
  Torn or cracked mounts
  Faults/looseness in clutch mechanism
  Shift linkage

## Slide 52: LO 13-4: Perform under-vehicle inspection.
Exhaust system inspection
  Look for signs of leaks, corrosion, or deteriorations
  Check heat shields
  Check exhaust pipe’s integrity
    Squeeze with arc joint pliers
    Squishy = needs replacing

## Slide 53: LO 13-4: Perform under-vehicle inspection.
Parking brake inspection
  Check for rusted, frozen, broken, or crushed cables
Fuel tank inspection
  Filler tube and hose
  Vent and fuel delivery lines
  Straps
  Protective shields
  Smell of gasoline = leak

## Slide 54: LO 13-5: Perform exterior vehicle inspection.
Exterior vehicle inspections
  Perform whenever a vehicle is in the shop
  Work in a systematic manner
  Use an inspection sheet to avoid missing anything

## Slide 55: LO 13-5: Perform exterior vehicle inspection.
Shock absorbers
  Often tested when there is unusual tire wear (appear cupped)
  Absorbers might bind up, causing stiff ride
  If adjustable absorbers, check that both sides are the same
  Uneven ride could mean some gas has leaked
  Modern and conventional shock absorbers
Bounce test
Visually inspect mounting points
Look for possible leaks

## Slide 56: LO 13-5: Perform exterior vehicle inspection.
Exterior lights inspection
  Done periodically to look for burnout
  Headlights, taillights, turn signals, side markers, brake lights, license plate lights, and backing lights
  Cornering lights, driving lights, or fog lights (in some vehicles)
  Check all rear light bulbs

## Slide 57: LO 13-5: Perform exterior vehicle inspection.
Wiper blades
  Missing, torn, worn could result in failed state inspection
  Usually replaced after a year
  Never operate when dry
  Never bend the arms
Avoid broken windshield
  Never let arm slip
  Place folded fender cover on windshield

## Slide 58: LO 13-5: Perform exterior vehicle inspection.
Windshield
  Inspect when checking wiper blades
  Polish may fix any scratches or pits
  Resin may repair small chips and cracks
  Otherwise replacement is needed

## Slide 59
Skill Drills

## Slide 60
Skill Drill 13-1: Checking Instrument Panel Warning Lamps

## Slide 61: Skill Drill 13-1: Checking Instrument Panel Warning Lamps
Perform an instrument panel self-test. When the key is switched on (before starting the engine), most of the dash warning lamps will light up as a bulb check. Note any that do not light up as expected.

## Slide 62: Skill Drill 13-1: Checking Instrument Panel Warning Lamps
Perform an engine running check. Start the engine and observe the warning lamps. All should go off after a few seconds as the related control module runs a self-check and then commands the lamp to go off.

## Slide 63
Skill Drill 13-2: Retrieving and Recording DTCs

## Slide 64: Skill Drill 13-2: Retrieving and Recording DTCs
Select the scan tool to provide the best coverage for the type and make of vehicle.

## Slide 65: Skill Drill 13-2: Retrieving and Recording DTCs
2. Locate the DLC and connect the scan tool.

## Slide 66: Skill Drill 13-2: Retrieving and Recording DTCs
3. Power on the scan tool.

## Slide 67: Skill Drill 13-2: Retrieving and Recording DTCs
4. Turn on the vehicle’s ignition. This should establish scan tool communication with the vehicle’s computer.

## Slide 68: Skill Drill 13-2: Retrieving and Recording DTCs
5. Retrieve and record the DTCs.

## Slide 69: Skill Drill 13-2: Retrieving and Recording DTCs
6. Power off the scan tool, turn off the ignition, and disconnect the scan tool.

## Slide 70
Skill Drill 13-3: Performing a Horn Check

## Slide 71: Skill Drill 13-3: Performing a Horn Check
Check the vehicle horn. Turn on the ignition and press the horn button. The horn should sound.
If the horn is not working, locate it under the hood with the help of the manufacturer’s service information. Check the wiring to make sure that it is connected securely.

## Slide 72
Skill Drill 13-4: Checking the Interior Lights

## Slide 73: Skill Drill 13-4: Checking the Interior Lights
1. Using the remote key fob or door key, unlock the doors. On most vehicles, this causes the interior lights to come on. Check that each light works as intended. On some vehicles, the lights do not come on until the door is opened. Check each door on the vehicle.

## Slide 74: Skill Drill 13-4: Checking the Interior Lights
Enter the vehicle and close the door. Wait to see that the lights go off after a time. Repeat this check with each door on the vehicle.

## Slide 75: Skill Drill 13-4: Checking the Interior Lights
Operate the courtesy lights from any other switches. Check the vanity lights and map lights, if equipped.

## Slide 76
Skill Drill 13-5: Using a Hydrometer to Measure the Freeze Protection Level

## Slide 77: Skill Drill 13-5: Using a Hydrometer to Measure the Freeze Protection Level
Select a hydrometer that is designed for use with the type of antifreeze being tested.

## Slide 78
Draw enough coolant into the hydrometer to bring it up to the fill line.
Skill Drill 13-5: Using a Hydrometer to Measure the Freeze Protection Level

## Slide 79: Skill Drill 13-5: Using a Hydrometer to Measure the Freeze Protection Level
Hold the hydrometer vertically and read the freeze protection level.

## Slide 80
Skill Drill 13-6: Using a Refractometer to Measure the Freeze Protection Level of Coolant

## Slide 81: Skill Drill 13-6: Using a Refractometer to Measure the Freeze Protection Level of Coolant
Remove the radiator cap and draw out a few drops of coolant.

## Slide 82
Place a drop or two of the coolant on the sample plate.
Skill Drill 13-6: Using a Refractometer to Measure the Freeze Protection Level of Coolant

## Slide 83
Close the diffuser plate, hold the refractometer level, look through the viewfinder, and read the scale.
Skill Drill 13-6: Using a Refractometer to Measure the Freeze Protection Level of Coolant

## Slide 84
Skill Drill 13-7: Checking Automatic Transmission Fluid Using a Dipstick

## Slide 85: Skill Drill 13-7: Checking Automatic Transmission Fluid Using a Dipstick
1. When checking transmission fluid, first wipe off the dipstick.

## Slide 86
Observe the markings.
Skill Drill 13-7: Checking Automatic Transmission Fluid Using a Dipstick

## Slide 87: Skill Drill 13-7: Checking Automatic Transmission Fluid Using a Dipstick
3. Reinsert the dipstick fully, remove it again, hold it horizontal, and read it.

## Slide 88
4. Turn over the dipstick and read the back side. The lowest reading between the front and the back is likely the most accurate reading.
Skill Drill 13-7: Checking Automatic Transmission Fluid Using a Dipstick

## Slide 89
Skill Drill 13-8: Checking and Refilling Windshield Washer Fluid

## Slide 90: Skill Drill 13-8: Checking and Refilling Windshield Washer Fluid
Locate the front windshield wiper fluid container.

## Slide 91
Check the windshield washer fluid level. If the level is low, refill the reservoir with the appropriate washer fluid.
Skill Drill 13-8: Checking and Refilling Windshield Washer Fluid

## Slide 92: Skill Drill 13-8: Checking and Refilling Windshield Washer Fluid
If equipped, check and fill the rear window washer reservoir.

## Slide 93
Skill Drill 13-9: Inspecting and Changing an Air Filter

## Slide 94: Skill Drill 13-9: Inspecting and Changing an Air Filter
On fuel-injected engines, unlatch or unscrew the filter housing fasteners to remove the air filter. It may be necessary to loosen the clamps and hoses on the induction tubing to remove the filter housing cover.

## Slide 95
On carbureted or throttle body-injected engines, remove the top of the air filter by unscrewing the wing nut, and remove the air filter.
Skill Drill 13-9: Inspecting and Changing an Air Filter

## Slide 96: Skill Drill 13-9: Inspecting and Changing an Air Filter
Inspect the air cleaner element by holding the filter element up to light and looking through it. If it is bright with no tears or cracks, it can be reused. If it is dark or damaged in any way, it needs to be replaced.

## Slide 97: Skill Drill 13-9: Inspecting and Changing an Air Filter
Clean the inside of the air filter housing, and inspect it and any ducts for cracks. If the air filter is being replaced, obtain a new air filter and compare it with the old one to ensure that they are exactly the same.

## Slide 98: Skill Drill 13-9: Inspecting and Changing an Air Filter
Place the new air filter inside the filter housing, making sure that it is aligned correctly on both sides.

## Slide 99: Skill Drill 13-9: Inspecting and Changing an Air Filter
Replace the cover of the air filter housing and tighten the latches, screws, or wing nut until completely closed. Reinstall any induction tubing or clamps.

## Slide 100
Skill Drill 13-10: Checking the Fluid Level of a Manual Transmission/Transaxle

## Slide 101: Skill Drill 13-10: Checking the Fluid Level of a Manual Transmission/Transaxle
1. Safely raise and support the vehicle on the lift so that it is level. Inspect the transmission for leaks. Remove the filler plug using the proper tool. Inspect the filler plug and fill hole for thread damage, and replace or repair if necessary.

## Slide 102: Skill Drill 13-10: Checking the Fluid Level of a Manual Transmission/Transaxle
2. If the gearbox fluid begins to run out as the filler plug is removed, let the gearbox fluid seek its own level before reinstalling the filler plug. The gearbox fluid level should be at the bottom of the fill plug hole.

## Slide 103: Skill Drill 13-10: Checking the Fluid Level of a Manual Transmission/Transaxle
3. If the fluid level is low, refill with the specified fluid, reinstall the filler plug, and wipe the area around the filler plug hole with a clean shop towel. Tighten the filler plug to the specified torque.

## Slide 104
Skill Drill 13-11: Checking and Adjusting the Differential Fluid Level

## Slide 105: Skill Drill 13-11: Checking and Adjusting the Differential Fluid Level
Safely raise and support the vehicle. Inspect the differential and transfer case for leaks. Position a clean drain pan under the filler plug. Using the correct tool, remove the filler plug. Inspect the filler plug threads for damage, and replace if necessary.

## Slide 106: Skill Drill 13-11: Checking and Adjusting the Differential Fluid Level
2. If the fluid begins to run out as the filler plug is removed, let the fluid seek its own level before reinstalling the filler plug. The fluid level should be at the bottom of the filler plug hole.

## Slide 107: Skill Drill 13-11: Checking and Adjusting the Differential Fluid Level
3. If the fluid level is low, refill with the specified fluid, reinstall the filler plug, and wipe the area around the filler plug hole with a clean shop towel. Tighten the filler plug to the specified torque.

## Slide 108
Skill Drill 13-12: Locating and Identifying Fluid Leaks

## Slide 109: Skill Drill 13-12: Locating and Identifying Fluid Leaks
1. Safely raise and support the vehicle on a lift. Use a light to check for fluid leaks at any place that fluids can leak.

## Slide 110: Skill Drill 13-12: Locating and Identifying Fluid Leaks
2. Once leaky fluid is found, follow it to its source.

## Slide 111: Skill Drill 13-12: Locating and Identifying Fluid Leaks
3. If it is hard to identify exactly where the leak is coming from, you may need to make it leak by pressurizing the cooling system, applying the brakes, or operating the leaking system.

## Slide 112: Skill Drill 13-12: Locating and Identifying Fluid Leaks
4. If you still cannot make it leak, try releasing the pressure or turning off the system. Sometimes leaks happen only when the system is shut off. This is a leak from the water pump weep hole.

## Slide 113
Skill Drill 13-13: Performing an Under-Vehicle Inspection

## Slide 114: Skill Drill 13-13: Performing an Under-Vehicle Inspection
Safely raise and secure the vehicle at a comfortable working height. Work systematically. Pay particular attention to any fluid leaks.

## Slide 115: Skill Drill 13-13: Performing an Under-Vehicle Inspection
Check the steering parts. Grasp the front and rear of the tire and pivot it to detect wear in the steering components. Grasp the tire at the top and bottom and pivot it to detect movement in the wheel bearings or ball joints. Look for missing or torn rubber boots around the tie-rod ends and steering rack. Inspect the rack bushings and other rubber suspension bushings.

## Slide 116: Skill Drill 13-13: Performing an Under-Vehicle Inspection
3. Inspect all four shock absorbers for signs of damage or leaks. Check the brake hoses and lines for signs of cracking, abrasions, or bulging.

## Slide 117
Check the front-wheel drive axles. On vehicles with front-wheel drive, examine the inner and outer CV boots for cracks or tears.
Skill Drill 13-13: Performing an Under-Vehicle Inspection

## Slide 118: Skill Drill 13-13: Performing an Under-Vehicle Inspection
5. Check the transmission area. Trace and record the source of fluid leaks. Check the mount. With a manual transmission, check the clutch operating mechanism for damage. For an automatic transmission, check the shift linkage for any damage. If the transmission is electronically controlled, check the wiring for damage.

## Slide 119
6. Check the exhaust system. Examine the catalytic converter, muffler, and resonator for signs of corrosion or deterioration. Inspect the heat shields. Check the tailpipe for corrosion, and check for damaged or missing hangers.
Skill Drill 13-13: Performing an Under-Vehicle Inspection

## Slide 120: Skill Drill 13-13: Performing an Under-Vehicle Inspection
Check the parking brake cables. Inspect the parking brake cable to make sure it is not frayed, damaged, or binding. Look for rusted or swollen cable housings. Pull on the cables, and check that the parking brake applies. Lubricate the cable if specified.

## Slide 121: Skill Drill 13-13: Performing an Under-Vehicle Inspection
8. Check the driveshaft. On rear-wheel drive vehicles, inspect the driveshaft universal joints for signs of excess movement or rust. To check for wear, rotate the shaft and flange in opposite directions (there should be no up-and-down or side-to-side movement). On four-wheel drive vehicles, inspect the front driveshaft universals.

## Slide 122: Skill Drill 13-13: Performing an Under-Vehicle Inspection
Check the differential and rear suspension area. Inspect the pinion shaft oil seal for any signs of leakage. Inspect the suspension mounting bushings for signs of deterioration or damage. If the vehicle is fitted with leaf springs, inspect them for any cracks or misalignment. Inspect the brake hoses for signs of cracking, abrasion, and bulges.

## Slide 123: Skill Drill 13-13: Performing an Under-Vehicle Inspection
Check the fuel tank area. Check all the fuel lines and brake lines for signs of damage, abrasions, leaks, or rust.

## Slide 124
Skill Drill 13-14: Performing a Visual Inspection of the Vehicle’s Exterior

## Slide 125: Skill Drill 13-14: Performing a Visual Inspection of the Vehicle’s Exterior
Prepare the vehicle. Park the vehicle in a well-lit area. Turn off the engine and unlock the doors and trunk or rear hatch.

## Slide 126: Skill Drill 13-14: Performing a Visual Inspection of the Vehicle’s Exterior
Walk around the vehicle, observing any obvious items that need attention. Check the body condition.

## Slide 127: Skill Drill 13-14: Performing a Visual Inspection of the Vehicle’s Exterior
Check exterior component and system operation.

## Slide 128: Skill Drill 13-14: Performing a Visual Inspection of the Vehicle’s Exterior
Open and close doors to check that they are operating correctly.

## Slide 129: Skill Drill 13-14: Performing a Visual Inspection of the Vehicle’s Exterior
Push and pull on the bumpers and fenders to ensure that they are secure.

## Slide 130: Skill Drill 13-14: Performing a Visual Inspection of the Vehicle’s Exterior
Inspect the external mirrors to ensure that they are secure and not broken.

## Slide 131
Skill Drill 13-15: Checking Shock Absorbers

## Slide 132: Skill Drill 13-15: Checking Shock Absorbers
Place your weight on a bumper, and begin to bounce the vehicle until it reaches its maximum amount of travel produced by your weight. Stop bouncing at the bottom of the bounce. If the shock absorbers are performing well, the vehicle will rebound once and then return to its original position.

## Slide 133: Skill Drill 13-15: Checking Shock Absorbers
Pay particular attention to the top strut mounting during the bounce test. Place your hand on top of the mounting during the bounce test. Any noise or looseness in the mounting could indicate the need to replace the mount.

## Slide 134: Skill Drill 13-15: Checking Shock Absorbers
Visually inspect the shock absorber mounting points for security and corrosion, and note any wet-looking patches on the sides of the shock absorbers. Slight dampness on the shock is typically normal, but a drip on the shock indicates leaking.

## Slide 135
Skill Drill 13-16: Checking the Exterior Lights

## Slide 136: Skill Drill 13-16: Checking the Exterior Lights
Have someone sit in the vehicle, turn the ignition on, and switch the light switch to the park light position. Check that the taillights, side markers, and rear license plate lights come on.

## Slide 137: Skill Drill 13-16: Checking the Exterior Lights
Put the turn signal switch in the left-turn and then in the right-turn position, and check that the signals flash equally on each side.

## Slide 138: Skill Drill 13-16: Checking the Exterior Lights
With the ignition key on and the engine off, place the transmission in reverse and observe the backup lights.

## Slide 139: Skill Drill 13-16: Checking the Exterior Lights
Depress the brake pedal to make sure the brake lights work. Check that the third (center) brake light works.

## Slide 140: Skill Drill 13-16: Checking the Exterior Lights
Make sure that the high and low headlight beams work properly.

## Slide 141: Skill Drill 13-16: Checking the Exterior Lights
Make sure that the park lights, side markers, turn indicators, and daytime running lamps (if equipped) are all working correctly.

## Slide 142
Skill Drill: 13-17: Checking and Replacing the Windshield Wiper Blades

## Slide 143: Skill Drill: 13-17: Checking and Replacing the Windshield Wiper Blades
Check the windshield wiper blades. Lift the wiper arm away from the windshield and inspect the condition of the blades. Look for damage or loss of resilience in the material.

## Slide 144: Skill Drill: 13-17: Checking and Replacing the Windshield Wiper Blades
Wet the windshield with a hose or with the washers and switch the wipers on. If the windshield is being wiped cleanly, do not replace the wiper blades. If the wiper blades are not wiping the glass evenly or are smearing, replace the blades.

## Slide 145: Skill Drill: 13-17: Checking and Replacing the Windshield Wiper Blades
Place a folded up fender cover under the wiper blade you are working on to protect the windshield.

## Slide 146: Skill Drill: 13-17: Checking and Replacing the Windshield Wiper Blades
Remove the blade assembly.

## Slide 147: Skill Drill: 13-17: Checking and Replacing the Windshield Wiper Blades
Obtain and install the appropriate replacement blades.

## Slide 148
Once the wiper blades are installed, test them for proper operation.
Skill Drill: 13-17: Checking and Replacing the Windshield Wiper Blades

## Slide 149
Skill Drill 13-18: Inspecting the Windshield

## Slide 150: Skill Drill 13-18: Inspecting the Windshield
Prepare the windshield. First, use glass cleaner to clean the windshield thoroughly.

## Slide 151
Inspect the glass. Look closely at the surface of the glass. It may help to use a flashlight or trouble light at an angle while inspecting.
Skill Drill 13-18: Inspecting the Windshield

## Slide 152: Skill Drill 13-18: Inspecting the Windshield
Look for any delamination conditions present.

## Slide 153: Credits
Unless otherwise indicated, all photographs and illustrations are under copyright of Jones & Bartlett Learning.