## Slide 1
Chapter 15
Low-Pressure Fuel Systems

## Slide 2: Introduction (1 of 2)
Diesel engines need low-pressure fuel systems to supply clean, cool, and air-free fuel to the high-pressure fuel system.

## Slide 3: Introduction (2 of 2)
Proper operation of low-pressure fuel system is critical to proper engine performance.

## Slide 4: Fundamentals of Low-Pressure Fuel Systems (1 of 3)
Requirements of Low-Pressure Fuel Systems
  Store and supply fuel free of contaminants and vapor
  Supply adequate fuel volume at the correct pressure to the high-pressure injection system
  Remove water contamination
  Prevent wax gelling
  Regulate fuel temperature

## Slide 5: Fundamentals of Low-Pressure Fuel Systems (2 of 3)
Fuel Temperature
  Changes in fuel temperature can affect engine power output and cause fuel to gel

## Slide 6: Fundamentals of Low-Pressure Fuel Systems (3 of 3)

## Slide 7: Components of Low-Pressure Fuel Systems (1 of 65)
Fuel Tanks
  Must store an adequate supply of fuel and allow it to cool
  Fuel that is too hot loses viscosity and density, reducing engine power
  2% power loss for every 10°F of fuel temperature above 115°F (46°C)

## Slide 8: Components of Low-Pressure Fuel Systems (2 of 65)
Fuel Tanks
  Tank Materials
    Aluminum, plastic, and steel alloys are most common
    Must meet minimum safety standards for on highway vehicles as set by federal authorities

## Slide 9: Components of Low-Pressure Fuel Systems (3 of 65)
Fuel Tank Ventilation
  Return fuel may need to release air and as level drops in tank air must replace void
  Fuel tank cap can incorporate relief valve and vacuum relief

## Slide 10: Components of Low-Pressure Fuel Systems (4 of 65)
Fuel Tank Ventilation
  Thermal plugs can be used to vent the tank when exposed to fire

## Slide 11: Components of Low-Pressure Fuel Systems (5 of 65)
Fuel Tank Ventilation
  Rollover protection valves prevent leakage
  Tanks must allow for expansion of fuel as it warms

## Slide 12: Components of Low-Pressure Fuel Systems (6 of 65)
Fuel Lines
  Fuel lines connect all low-pressure components
  Can be braided steel, steel tube, rubber, or nylon plastic (Synflex)
  All diesel fuel compatible
  Must be routed away from damage and allow for some movement

## Slide 13: Components of Low-Pressure Fuel Systems (7 of 65)
Fuel Tank Pickup and Sending Unit
  Integrated with a level sensing device

## Slide 14: Components of Low-Pressure Fuel Systems (8 of 65)
Fuel Tank Pickup and Sending Unit
  May include filters, regulators, pumps, and reservoirs

## Slide 15: Components of Low-Pressure Fuel Systems (9 of 65)
Tank Pickup
  Place just above bottom of tank to prevent contamination

## Slide 16: Components of Low-Pressure Fuel Systems (10 of 65)
Tank Pickup
  Heavy-duty vehicle tanks use pickups located at top

## Slide 17: Components of Low-Pressure Fuel Systems (11 of 65)
Tank Pickup
  Large tanks will have a tank drain located at the lowest point of tank

## Slide 18: Components of Low-Pressure Fuel Systems (12 of 65)
Dual Fuel Tank Pickups
  Heavy-duty vehicles may have dual tanks with pickups

## Slide 19: Components of Low-Pressure Fuel Systems (13 of 65)
Dual Fuel Tank Pickups
  Return flow splitter valve keeps level in tanks; eliminates crossover line

## Slide 20: Components of Low-Pressure Fuel Systems (14 of 65)
Fuel Return Circuits
  Most fuel systems circulate fuel through the high-pressure system to lubricate and cool components
  Newer systems reduce amount of fuel circulated

## Slide 21: Components of Low-Pressure Fuel Systems (15 of 65)
Sending Units
  Transmit electrical signal for fuel level to a dash gauge

## Slide 22: Components of Low-Pressure Fuel Systems (16 of 65)
Sending Units
  Most common type is variable resistance: float moves with fuel level and gauge circuit resistance changes

## Slide 23: Components of Low-Pressure Fuel Systems (17 of 65)
Sending Units
  Can be part of HD-ODB system to help diagnose low power problems
  Can be part of CAN bus system

## Slide 24: Components of Low-Pressure Fuel Systems (18 of 65)

## Slide 25: Components of Low-Pressure Fuel Systems (19 of 65)
Fuel Filters
  Requirements
  Fuel quality is key to reliability and durability of fuel system components

## Slide 26: Components of Low-Pressure Fuel Systems (20 of 65)
Fuel Filters
  Requirements
    Fine abrasive wear caused by contamination
    Particles 5–7 microns in size cause most damage
    Fuel system wear can cause high fuel, consumption,­ hard starting, rough idle, reduced engine power, increased smoke, and other exhaust emissions

## Slide 27: Components of Low-Pressure Fuel Systems (21 of 65)
Fuel Filters
  Contamination Sources
    Asphaltenes
      Soft particles that occur naturally in 2-D diesel fuel
      High heat and oxidation increases content
      1.5–2 microns in diameter

## Slide 28: Components of Low-Pressure Fuel Systems (22 of 65)
Fuel Filters
  Contamination Sources
    Water—most destructive contaminant

## Slide 29: Components of Low-Pressure Fuel Systems (23 of 65)
Fuel Filters
  Contamination Sources
    Water—can seize injectors

## Slide 30: Components of Low-Pressure Fuel Systems (24 of 65)
Fuel Filters
  Contamination Sources
    Water
      Causes loss of film strength of diesel fuel; loss of lubricity
      Helps form acid
      Causes rust
      Helps microorganism growth
      Fuel filters can separate water and fuel via coalescences or centrifugal methods

## Slide 31: Components of Low-Pressure Fuel Systems (25 of 65)

## Slide 32: Components of Low-Pressure Fuel Systems (26 of 65)

## Slide 33: Components of Low-Pressure Fuel Systems (27 of 65)

## Slide 34: Components of Low-Pressure Fuel Systems (28 of 65)

## Slide 35: Components of Low-Pressure Fuel Systems (29 of 65)
Fuel Filters
  Contamination Sources
    Water
      Filter drain valves allow draining of water from filter housing
      WIF sensors alert operator to water in fuel by either float or electrical conductivity difference

## Slide 36: Components of Low-Pressure Fuel Systems (30 of 65)

## Slide 37: Components of Low-Pressure Fuel Systems (31 of 65)

## Slide 38: Components of Low-Pressure Fuel Systems (32 of 65)
Fuel Filters
  Contamination Sources
    Bacteria and Fungi
      Grow in fuel under the right conditions and if fuel is left stagnant
      Fuel can be treated with biocide

## Slide 39: Components of Low-Pressure Fuel Systems (33 of 65)
Fuel Filters
  Contamination Sources
    Wax
      Solidifies at cold temperature
      At 32*F, 2-D becomes cloudy (cloud point)
      Fuel should be blended for seasonal and regional conditions

## Slide 40: Components of Low-Pressure Fuel Systems (34 of 65)
Fuel Filters
  Contamination Sources
    Wax
      Fuel heaters can be in filter housing and electric

## Slide 41: Components of Low-Pressure Fuel Systems (35 of 65)
Fuel Filters
  Contamination Sources
    Wax
      Fuel heaters can use coolant

## Slide 42: Components of Low-Pressure Fuel Systems (36 of 65)
Fuel Filters
  Filter Media
    Paper (cellulose), microglass, cotton, felt, wood
    Openings allow fuel through but trap small particles
    Surface area holds contaminants for one service interval

## Slide 43: Components of Low-Pressure Fuel Systems (37 of 65)
Fuel Filters
  Filter Media
    Paper (cellulose), microglass, cotton, felt, wood
    Openings allow fuel but trap small particles
    Surface area holds contaminants for one service interval
    Paper: least expensive
    Microglass: most effective, most common

## Slide 44: Components of Low-Pressure Fuel Systems (38 of 65)
Fuel Filters
  Efficiency
    Absolute micron rating determines percentage of largest particle sizes a filter will allow to pass through

## Slide 45: Components of Low-Pressure Fuel Systems (39 of 65)

## Slide 46: Components of Low-Pressure Fuel Systems (40 of 65)
Fuel Filters
  Primary and Secondary Filters
    Primary filter located between tank and transfer pump inlet; 95-98% efficient at 10-100 microns
    Secondary filter located between transfer pump outlet and high-pressure fuel system components

## Slide 47: Components of Low-Pressure Fuel Systems (41 of 65)
Fuel Filters
  Cartridge Filter
    Spin on filters are not environmentally friendly and make cartridge filters more popular
    Can prevent engine from starting if filter not in place

## Slide 48: Components of Low-Pressure Fuel Systems (42 of 65)
Fuel-Water Separators and Heaters
  Fuel Heaters
    Reduce and eliminate fuel gelling, which clogs filters and causes hard starting or no starting
    Can be electric or use engine coolant to warm fuel

## Slide 49: Components of Low-Pressure Fuel Systems (43 of 65)
Fuel-Water Separators and Heaters
  Fuel-Water Separators
    Water removal from fuel is critical for fuel system longevity
    Use coalescence to remove water
    Centrifugal filters can assist with water removal

## Slide 50: Components of Low-Pressure Fuel Systems (44 of 65)
Fuel-Water Separators and Heaters
  Water-in-Fuel Sensors
    Use an electrical conductivity probe
    Signal sent triggers a dash light

## Slide 51: Components of Low-Pressure Fuel Systems (45 of 65)
Fuel-Water Separators and Heaters
  Fuel-Water Separator and Heater Modules
    One module can combine one or more filters, fuel-water separators, water-in-fuel sensors, fuel heaters

## Slide 52: Components of Low-Pressure Fuel Systems (46 of 65)
Fuel Transfer Pumps
  Move fuel from tank to high-pressure system
    Gear Pumps
      Positive displacement pump with two gears

## Slide 53: Components of Low-Pressure Fuel Systems (47 of 65)

## Slide 54: Components of Low-Pressure Fuel Systems (48 of 65)
Fuel Transfer Pumps
  Gear Pumps
    Fuel is carried around outside of teeth from pump inlet to outlet
    Fuel flow is proportional to pump rpm
    Check valves at inlet allow priming pump to bypass gear pump

## Slide 55: Components of Low-Pressure Fuel Systems (49 of 65)

## Slide 56: Components of Low-Pressure Fuel Systems (50 of 65)
Fuel Transfer Pumps
  Gear Pumps
    Return restriction will regulate system pressure

## Slide 57: Components of Low-Pressure Fuel Systems (51 of 65)

## Slide 58: Components of Low-Pressure Fuel Systems (52 of 65)
Fuel Transfer Pumps
  Gear Pumps
    Can incorporate electric priming pump to eliminate gear pump starvation

## Slide 59: Components of Low-Pressure Fuel Systems (53 of 65)
Fuel Transfer Pumps
  Mechanical Diaphragm Pump
    Common type of low-pressure pump

## Slide 60: Components of Low-Pressure Fuel Systems (54 of 65)

## Slide 61: Components of Low-Pressure Fuel Systems (55 of 65)
Fuel Transfer Pumps
  Mechanical Diaphragm Pump
    Cam-actuated arm moves diaphragm against spring pressure
    Movement of diaphragm creates pressure differential to move fuel from tank to pump inlet

## Slide 62: Components of Low-Pressure Fuel Systems (56 of 65)
Mechanical Diaphragm Pump
  Variable Displacement in a Diaphragm Pump
    As volume output exceeds demand linkage, diaphragm remains stationary and does not pump fuel
    Most pumps incorporate hand-lever prime pump

## Slide 63: Components of Low-Pressure Fuel Systems (57 of 65)
Piston-Type Pumps
  Use a piston to create pressure differential

## Slide 64: Components of Low-Pressure Fuel Systems (58 of 65)

## Slide 65: Components of Low-Pressure Fuel Systems (59 of 65)
Piston-Type Pumps
  Used for higher pressure applications

## Slide 66: Components of Low-Pressure Fuel Systems (61 of 65)

## Slide 67: Components of Low-Pressure Fuel Systems (62 of 65)
In-Tank Electric Pumps
  Medium-duty vehicles will use in-tank pumps
  Pressurizes entire system
  Makes priming system easy

## Slide 68: Components of Low-Pressure Fuel Systems (63 of 65)
Fuel Coolers
  Pressurizing diesel fuel heats it up
  Coolers are needed to keep fuel below flash point of 140*F
  Detroit Diesel DD series use coolant-cooled coolers

## Slide 69: Components of Low-Pressure Fuel Systems (64 of 65)
Roller Vane Pumps
  Most in-tank pumps are driven by permanent magnet motors
  Vanes are carried around pump housing and move fuel past check valves to pump outlet

## Slide 70: Components of Low-Pressure Fuel Systems (65 of 65)
Vane-Type Pumps
  Some injection pumps have mechanical vane pumps; some pumps are electrically driven
  Can be electronically controlled to prevent over-pressurization

## Slide 71: Maintenance of Low-Pressure Fuel Systems (1 of 22)
Evaluating engine performance problems often leads to checking low-pressure fuel system operation
Pressure and flow can be measured

## Slide 72: Maintenance of Low-Pressure Fuel Systems (2 of 22)

## Slide 73: Maintenance of Low-Pressure Fuel Systems (3 of 22)
Checking for air in fuel is common practice

## Slide 74: Maintenance of Low-Pressure Fuel Systems (4 of 22)
Filter restrictions can be measured using gauges or by viewing electronic data

## Slide 75: Maintenance of Low-Pressure Fuel Systems (5 of 22)
Filter restrictions can be measured using gauges or by viewing electronic data

## Slide 76: Maintenance of Low-Pressure Fuel Systems (6 of 22)

## Slide 77: Maintenance of Low-Pressure Fuel Systems (7 of 22)

## Slide 78: Maintenance of Low-Pressure Fuel Systems (8 of 22)
Detroit Diesel FSIC Test
  FSIC (fuel system integrity check) is used to identify fuel system problems
  A laptop and diagnostic software is needed
Malfunctioning Fuel Tank Vent
  Can lead to negative tank pressure and fuel starvation

## Slide 79: Maintenance of Low-Pressure Fuel Systems (9 of 22)
Air Leaks on Suction Lines
  Lines that connect the tank to transfer pump inlet are at negative pressure when engine is running
  Air can be drawn into these lines and lead to low power or damaged components

## Slide 80: Maintenance of Low-Pressure Fuel Systems (10 of 22)

## Slide 81: Maintenance of Low-Pressure Fuel Systems (11 of 22)
Filter Service
  Filter efficiency increases as filters capture contamination
  Fuel filters don’t have bypass valves; plugged filters will affect engine performance

## Slide 82: Maintenance of Low-Pressure Fuel Systems (12 of 22)

## Slide 83: Maintenance of Low-Pressure Fuel Systems (13 of 22)
Common Fuel System Problems
  Filters should be replaced at recommended intervals
  Measured in inches of water or mercury

## Slide 84: Maintenance of Low-Pressure Fuel Systems (14 of 22)
Performing a Primary Fuel Filter Suction-Side Pressure Test
  Should not provide excessive restriction to transfer pump
  Install vacuum gauge at filter outlet and run engine at high idle

## Slide 85: Maintenance of Low-Pressure Fuel Systems (15 of 22)
Measuring Primary Filter Restriction
  Install gauges on both sides of primary filter and compare
Performing a Primary Fuel Filter Suction-Side Restriction Test
  Can indicate a restriction in line between primary filter and tank
  Install vacuum gauge at filter inlet and run engine at rated speed
  10” maximum allowable

## Slide 86: Maintenance of Low-Pressure Fuel Systems (16 of 22)
Measuring Secondary Filter Output Pressure
  Low reading will indicate plugged filter
  Install pressure gauge at filter outlet and run engine at high idle
  50-80 psi acceptable

## Slide 87: Maintenance of Low-Pressure Fuel Systems (17 of 22)
Diaphragm Pump Problems
  Check valves can deteriorate, reducing pump flow
  Can result in hard starting and low power
  Springs can break
  External oil or fuel leaks

## Slide 88: Maintenance of Low-Pressure Fuel Systems (18 of 22)
Oil Contamination of Fuel
  Can come from transfer pumps, HEUI injectors
  Can be detected with paper towel test or oil sample

## Slide 89: Maintenance of Low-Pressure Fuel Systems (19 of 22)
Priming Fuel Systems
  Must be done when an engine runs out of fuel or after servicing or rebuild
  Priming pump is used with bleeder screw open

## Slide 90: Maintenance of Low-Pressure Fuel Systems (20 of 22)

## Slide 91: Maintenance of Low-Pressure Fuel Systems (21 of 22)
Replacing a Fuel Filter and Priming a Fuel System
  Carefully replace filter according to engine service information
  Prime fuel system using recommended procedures

## Slide 92: Maintenance of Low-Pressure Fuel Systems (22 of 22)
Hard Starting Problems
  Can include fuel leak back to the tank, air in the fuel system, low or no fuel pressure, inadequate fuel delivery volume
  Check for loose, kinked, cracked lines, plugged filters, defective pump, and/or valve

## Slide 93: Summary (1 of 8)
Diesels need a low-pressure fuel supply to transfer fuel from the fuel tank with adequate volume and pressure to the high-pressure injection stage of the fuel system.
Proper operation and service of the low-pressure fuel supply system is critical to quick starting, engine durability, and reliable, trouble-free operation of diesel- powered vehicles.

## Slide 94: Summary (2 of 8)
The functions of the low-pressure fuel system include storing and supplying fuel free of contaminants and vapor at the correct pressure to the high-pressure injection system, removing water contamination, preventing fuel wax from gelling, and regulating fuel temperature.

## Slide 95: Summary (3 of 8)
While the most obvious function of the fuel tank is to store an adequate supply of fuel for the engine’s application, a secondary function is to allow fuel returned from the engine to cool after absorbing heat from the engine and fuel injectors.

## Slide 96: Summary (4 of 8)
Low-pressure fuel transfer lines connect the fuel circuits of the low-pressure transfer system.
Fuel tank pickups can be integrated with a fuel level– sending unit and fuel transfer pump; these modules may include several components that may or may not be separately serviceable.

## Slide 97: Summary (5 of 8)
Fuel filters remove dirt contamination from fuel that could cause abrasive wear of injection components.
The most common contaminants found in today’s fuels are asphaltene, air, water, microorganisms, and wax.

## Slide 98: Summary (6 of 8)
To prepare fuel for cold weather use and avoid operating difficulties, the low-pressure supply system is oft en equipped with a variety of devices to condition the fuel by removing water and dissolving wax.
Fuel transfer pumps are used to move fuel from the fuel tanks to the high-pressure fuel system; the fuel must be supplied with adequate volume at the correct pressure for every operating condition.

## Slide 99: Summary (7 of 8)
A variety of pump types exist to match the unique requirements of each high-pressure fuel system.
Evaluating the operation of the low-pressure supply system is indicated when investigating complaints regarding low power, hard or prolonged starting, rough engine operation, and failures of high-pressure injection components.

## Slide 100: Summary (8 of 8)
Whenever fuel filters are replaced, or if an engine has run out of fuel, the system usually needs to have air purged from the filter and lines in order to start.